## Slide 1: Risk happens --- and formal methods can help Enno Ruijters Formal Methods & Tools

## Slide 2: Introduction

## Slide 3: No risk, no fun

## Slide 4
sensors
object detection
GPS
lasers
software
How to manage risks of (new) products & services?
Model risks
Analyze / prioritize
Take appropriate measures
Design space: improve safety (& security)
Better components | redundancy | fail-safe mechanisms | maintenance | testing | ….
 Make better and more informed decisions

## Slide 5: Risk priority heat map
Probability
Severity / impact
driving license,
ad. cruise control
Speed limits
Airbags
Accept risks
Insure

## Slide 6: How to get the heat map?

## Slide 7: WHO AM I ?
2014 – 2018
PhD Student: ArRangeer project
Formal Methods and Tools @ UTwente
Integrating maintenance in fault trees
Collaboration with ProRail and NedTrain
2018 – now
Postdoc @ Utwente
Software testing based on user actions
2008 – 2014: Operations Research
Maastricht University

## Slide 9: Risk management: engineering a safer world
Methods
Informal / Spread sheets:
  Failure Mode, Effect and Criticality Analysis (FMECA)
  Hazard & operability study (Hazop)
Architectural:
  UML/Marte,
  AADL
Domain-specific:
  Fault tree analysis
  Reliability block diagrams,
  Event trees
Formal Methods can help!
Risk assessment often mandatory
Standardization
NRC NUREG–0492: nuclear industry
SAE ARP4761: aerospace,
IEC standard: 61025
European NEN 61025.
Design alternatives
More redundancy
Hot / warm / cold spare components
More reliable components
Monitoring
Fail-safe mechanisms

## Slide 10: Do things you could not do before
Use FME(C)A to get an overview of risks
Model & analyze risk quantitatively via fault trees
Calculate possible outcomes via event trees
Be fluent on probability theory
Theory + practice = fun!

## Slide 11: Other quantitative methods
Not covered:
Financial models
Human factors analysis
  Aerospace, nuclear industries
Software reliability
Physics of failure
Plenty of others 

## Slide 12: Overview
FTs
standard
dynamic
qualitative
quantitative
discrete
probability
continuous
probability
cut sets
qualitative
quantitative
discrete
probability
continuous
probability
cut sequence
Risk analysis
FME(C)A / HAZOP

## Slide 14: FME(C)A & HAZOP
Note: related to Attack Trees in security

## Slide 15: Failure Mode and Effect Analysis
Spreadsheet based method
Enumerate all (single) failure modes and their effects
Different standard have different fields
Example (for this presentation):
Component | Failure mode | Effect
Projector | Lamp fails | Change rooms, delay
Computer | Does not start | Use different computer
Laser pointer | Empty batteries | Point manually
Presenter | Oversleeps | Late start

## Slide 16: Failure Mode, Effect and Criticality Analysis
Extend FMEA with probability and severity:
Component | Failure mode | Effect | Prob. | Severity | Criticality
Beamer | Lamp fails | Change rooms, delay | Low | Medium | Low
Computer | Does not start | Use different computer | Medium | Medium | Medium
Laser pointer | Empty batteries | Point manually | High | Low | Medium
Presenter | Oversleeps | Late start | Low | High | Medium

## Slide 17: Failure Mode and Effect Analysis
Other fields sometimes included:
  Function (of system and/or component)
  Failure cause
  Consequences of different types (e.g. cost, risk to public, reputation damage, etc.)
  Mitigation, residual effects
  Detection options
  Other internal fields (reporting codes, historic occurrence, etc.)

## Slide 18: Failure Mode and Effect Analysis
More detailed example:
Component | Function | Failure mode | Failure cause | Local effect
Beamer | Show presentation | Blank screen | Lamp burnt out | No visuals
Computer | Show presentation | Does not start | Windows | No visuals
Laser pointer | Direct attention | Does not point | Batteries empty | Manual pointing
Presenter | Teach | Oversleeps | Alarm clock fails | Late start
Mitigation | Residual effect | Global effect
Change rooms | Delay | Students learn less
Use other computer | Delay | Students learn less
Use spare batteries | None | Presenter has tired arm
None | Late start | Students learn less

## Slide 19: Failure Mode and Effect Analysis (Exercise)
Perform FMECA for a bicycle.
Fields:
  Component
  Function
  Failure mode
  Global effect
  Probability (high/medium/low)
  Severity (high/medium/low)
Find approx. 5 lines

## Slide 20: Failure Mode and Effect Analysis
My FMECA:
Your answers may differ
Component | Function | Failure mode | Effect | Prob. | Severity
Tire(s) | Smooth ride | Puncture | Bumpy ride | High | Medium
Brake(s) | Slow down | Cable severed | Accident | Low | High
Lamp | Draw attention, avoid fines | Burnt out bulb | No cycling in dark | Medium | Medium
Bell | Draw attention | Broken clapper | Stuck behind slower traffic | Medium | Low
Chain | Speed up | Slipped off gear | Stopped until fixed | High | Medium
Chain | Speed up | Broken link | Stopped until replaced | Low | High

## Slide 21: Hazard and operability study (HAZOP)
Similar to FME(C)A.
Commonly used in chemical industry
Systematic method to enumerate failure modes using guide words
List of possible components:
  Cooling, heating, power, reactants, etc.
List of possible conditions:
  Too much, not enough, incorrect, etc.
Identify all applicable combinations

## Slide 22: Hazard and operability study (HAZOP)
Example (baking bread):
Condition | Component | Effect | Etc.
Not enough | Flour | Crumbly bread | 
Too much | Flour | Very dense bread | 
Not enough | Heating | Raw dough in bread | 
Too much | Heating | Burnt bread | 
Too fast | Heating | Burnt crust and raw dough | 

## Slide 24: fault trees
Note: related to Attack Trees in security

## Slide 25: Fault trees: what are they?
Tool in reliability engineering
Graphical Model
  Tell how systems fail:
  How do component failures lead to system failures?
Qualitative Analysis
  Pinpoint root causes / critical parts
Quantitative Analysis: metrics
  Reliability: P[no failure during mission time]
  Availability: E[up-time]
  MTTF
  …
Read more?
Overview state-of-the-art modeling, analysis, tools
> 150 FT papers

## Slide 26: fault trees: who uses them?

## Slide 27
FTA on twitter
Falcon 7 rocked, SpaceX
Led by Elon Musk, Tesla
Ready for launch June 2015

## Slide 28: Fault trees
Describe how component failures interact.
Building blocks:
Start with undesired event and repeatedly break down into possible causes.
Or gate
AND gate
2/5
VOTING gate
Basic event

## Slide 29: Example: Safe road trip
road trip fails
car
tire 1
tire 2
tire 3
tire 4
spare
2/5
phone
connection
power
engine
battery
tires
Cut sets: Which BEs make FT fail?
{battery, engine, tire 1, spare}
{no connection, engine} minimal cut set
{connection, tire 1, spare} minimal cut set

## Slide 30: (Minimal) cut sets
Cut set
Set of basic events C that cause the FT to fail
Minimal cut sets
Cut set that is minimal, ie no proper subset of C is cut set
Use of minimal cut sets
Validation of fault trees
  If all BEs in C fail, should the system fail?
Identify weak points:
  too small cut sets
  Interpretation by experts: is this acceptable?

## Slide 31: The fault tree model: semantics
Structure function Φ: {0,1}#BEs  {0,1}
1 = fail; 0 = operational
Given values e1, …en, does F fail?
πF: P(BE)  {0,1}
If BEs e1, …en fail, does F fail?
πF: P(BE) x Elt  {0,1}
If BEs e1, …en fail, does e fail?
Recursive characterization
  AND-case: πF(E,e) = 1 iff πF(E,e’) = 1 for all children e’ of e
  … etc ..
Cut set : Set of basic events C that cause FT to fail: πF(C) = 1
  FTs are coherent:
    S ≤ S’ & πF(S)= 1  πF(S’) = 1
    Non-coherent extensions exist (eg NOT, XOR gate)
e2
e1
en
e
road trip

## Slide 32: Exponential probability distribution
Components fail with fixed rate / time
Unreliability / CDF =
P[fail before x] =
P[X ≤ x] = 1 − e−λx
Reliability =
P[no fail before x] =
P[X > x] = e−λx
PDF
f(x) = F’(x) = λe−λx
Who is afraid of
probability theory?

## Slide 33
How to determine system reliability?
= probability of no failure during mission time

## Slide 34: Quiz question #1: determine unreliability / failure probability
p2
road trip
car
p4
tire 1
p4
tire 2
p4
tire 3
p4
tire 4
p4
spare
2/5
phone
power
p3
engine
battery
tires
p1
connection
p2p3
p1 + p2p3 - p1p2p3
P[A v B ] = P[A] + P[B] – P[A&B]
P[A & B ] = P[A] P[B], A, B indep
1 – (1-p4)5 – 5p4(1-p4)4
1 – (1-p3)((1-p4)5 + 5p4(1-p4)4)
P[A ] = P[A | B] P[B] + P[A|BC] P[BC]
??
(p1 + p2 - p1p2)p3 +
p1(1 – ((1-p4)5 + 5p4(1-p4)4)(1-p3)
P[BC] = 1 – P[B]

## Slide 35: Speed up #1: discard (higher order) products
p2
road trip
car
p4
tire 1
p4
tire 2
p4
tire 3
p4
tire 4
p4
spare
2/5
phone
power
p3
engine
battery
tires
p1
connection
p2p3
p1 + p2p3 - p1p2p3
1 – (1-p4)5 – 5p4(1-p4)4
1 – (1-p3)((1-p4)5 + 5p4(1-p4)4)
??
(p1 + p2 - p1p2)p3 +
p1(1 – ((1-p4)5 + 5p4(1-p4)4))(1-p3)
p1+p2 - p1p2
Case 1: engine fails; p3=1
1
(p1+p2 - p1p2)p3
Case 2: engine does not fail; p3=0
p1
1 – ((1-p4)5 + 5p4(1-p4)4)
p1(1 – ((1-p4)5 + 5p4(1-p4)4)) (1-p3)
P[A ] = P[A | B] P[B] + P[A|BC] P[BC]

## Slide 36
Find 3 ways to speed up this computation
Quiz question #2:

## Slide 37: Simplify the computation
Disregard higher order products
Use minimal cut sets
Combine 1 & 2
Use BDDs

## Slide 38: Speed up #1: discard (higher order) products
p2
road trip
car
p4
tire 1
p4
tire 2
p4
tire 3
p4
tire 4
p4
spare
2/5
phone
power
p3
engine
battery
tires
p1
connection
p2p3
p1 + p2p3 - p1p2p3
1 – (1-p4)5 – 5p4(1-p4)4
1 – (1-p3)((1-p4)5 + 5p4(1-p4)4)
??
(p1 + p2 - p1p2)p3 +
p1(1 – ((1-p4)5 + 5p4(1-p4)4)(1-p3)
0
p1
5p4– 5p4 = 0
1 – (1-p4)5 < 5p4
p3
p1+ p3

## Slide 39
Speed up #2 & 3: Using cut sets
p2
road trip
car
p4
tire 1
p4
tire 2
p4
tire 3
p4
tire 4
p4
spare
2/5
phone
power
p3
engine
battery
tires
p1
connection
(p1 + p2 - p1p2)p3 +
p1(1 – ((1-p4)5 + 5p4(1-p4)4)(1-p3)
Min cut set | prob
connection, engine | p1 * p3
battery, engine | p2 * p3
connection, t1, t2 | p1 * p42
connection, t1, t3 | p1 * p42
connection t1, t4 | p1 * p42
connection t1, spare | p1 * p42
connection t2, t3 | p1 * p42
connection t2, t4 | p1 * p42
connection t2, spare | p1 * p42
connection t3, t4 | p1 * p42
connection t3, spare | p1 * p42
connection t4, spare | p1 * p42
TOTAL | p1*p3 + p2*p3 + 10* p1 * p42
Note: p1 , p4
should be low
Under- or overapproximation? Why?
P[C1 v C2 v C3 ] =
P[C1] + P[C2] + P[C3]
- P[C1]P[C2] - P[C1]P[C2] - P[C2]P[C2]
+ P[C1] P[C2] P[C3] ≤
P[C1] + P[C2] + P[C3]
Combine with #3

## Slide 40: Speed up #2 & 3: Using BDDs
BDDs
Compact representation for Boolean functions f(x1,x2,….,xn)
  eg the structure function of a FT
Heavily used in model checking
  (intial) condition
  (reachable) state space
Based on Shannon expansion / pivotal decomposition
  f(x1,x2,….,xn) = x1f(0,x2,….,xn) + x1f(1,x2,….,xn)
  fixed variable ordering
  shared subtrees

## Slide 41: Example: (x1 OR x2) AND x3
Truth Table
Decision Tree
  Vertex represents decision
  Follow dashed line for value 0
  Follow solid line for value 1
  Function value in leave.
x1 | x2 | x3 | f(x1,x2,x3)
0 | 0 | 0 | 0
0 | 0 | 1 | 0
0 | 1 | 0 | 0
0 | 1 | 1 | 1
1 | 0 | 0 | 0
1 | 0 | 1 | 1
1 | 1 | 0 | 0
1 | 1 | 1 | 1
x2
x3
x3
x3
x3
x1
1
1
1
0
0
0
0
0
x2

## Slide 42: Example: (x1 OR x2) AND x3
x2
x3
x3
x3
x3
x1
0
x2
Variables ordered
x1 < x2 < x3
(no OR x2) AND x3 = x2 AND x3
(yes OR x2) AND x3 = x3
x3
x3
0
0
0
0
1
1
1
yes AND x3 = x3
no AND x3 = no

## Slide 43: Example: (x1 OR x2) AND x3
x2
x3
x3
x3
x3
x1
0
x2
Variables ordered
x1 < x2 < x3
1

## Slide 44: Example: (x1 OR x2) AND x3
x3
x1
1
0
x2
Variables ordered
x1 < x2 <….,< xn
function value at leaves
x1 = 0
x1 = 1
Size of BDDs heavily
depends on variable order
x1 < x2 <….,< xn
Finding best order is
NP hard
Good algos in practice

## Slide 45: Using BDDs
p2
road trip
car
p4
tire 1
p4
tire 2
p4
tire 3
p4
tire 4
p4
spare
2/5
phone
power
p3
engine
battery
tires
p1
connection
engine
connection
1
0
battery
p1
p3
p2
1-p1
(connection + battery ) & engine
p3p1 + p3p2(1-p1)
BDDs also find MCS

## Slide 46: Event trees

## Slide 47: Event trees
Describe possible consequences of events.
Quantitative if probabilities known
Process:
  Start with initiating event.
  Determine possible immediate consequences.
  Examine what decides which consequences occur.
  Repeat

## Slide 48: Event trees (example)
Fire
Building occupied
Building not occupied
Firefighters arrive quickly
Firefighters arrive slowly
Building severely damaged
Deaths
Building somewhat damaged

## Slide 49: Event trees quantification
Assign probabilities to conditions
Fire
Building occupied
Building not occupied
Firefighters arrive quickly
Firefighters arrive slowly
Building severely damaged
Deaths
Building somewhat damaged
60%
40%
90%
10%

## Slide 50: Event trees quantification
Compute probabilities of outcomes
Fire
Building occupied
Building not occupied
Firefighters arrive quickly
Firefighters arrive slowly
Building severely damaged
Deaths
Building somewhat damaged
60%
40%
90%
10%
0.6 x 0.9 = 0.54
0.6 x 0.1 = 0.06
0.4

## Slide 51: Event trees quantification
Assign impact and compute risk
Fire
Building occupied
Building not occupied
Firefighters arrive quickly
Firefighters arrive slowly
Building severely damaged
Deaths
Building somewhat damaged
60%
40%
90%
10%
0.6 x 0.9 = 0.54
0.6 x 0.1 = 0.06
0.4
€50,000
€500,000
€10,000,000
0.54 x 50,000 + 0.06 * 10,000,000 + 0.4 * 500,000 = €827,000
If a fire occurs

## Slide 52: Bow-tie diagram
Combine fault tree and event tree
  Use fault tree to analyze occurrence of initiating event.
  Use event tree to analyze consequences of event.

## Slide 53: Bow-tie diagram (example)

## Slide 54: fault trees in continuous time

## Slide 55: System (un)reliability
Unreliability
  U(t) = P[failure before time t]
Reliability / Survivor function
  R(t) = P[no failure until time t]
  = 1- U(t)
t
U(t)

## Slide 56: Continuous probability: failure behaviour over time
road trip
car
tire 1
tire 2
tire 3
tire 4
spare
2/5
phone
power
engine
battery
tires
connection

## Slide 57: Continuous probability distributions: which one?
Uniform distribution
Gaussian
Exponential
  realistic model for degradation
  mathematically tractable
  approximation via composed exponentials
Weibull
  generalized exponential
  often used
  not discussed

## Slide 58: Repap: Continuous probability distributions
Often: P[X = x] = 0
Hence: F(x) = P[X ≤ x]
P[x ≤ X ≤ y] = P[X ≤ y] – P[X>x]
Where does the probability increase most?
  f(x) = F’(x)
  Then F(x) = the area under the graph

## Slide 59: Bath tub curve: degradation behaviour of systems
exponential

## Slide 60: Exponential probability distribution
Components fail with fixed rate / time
Unreliability / CDF =
P[fail before x] =
P[X ≤ x] = 1 − e−λx
Reliability =
P[fail before x] =
P[X > x] = e−λx
PDF
f(x) = F’(x) = λe−λx
Exponential is a fundamental probability distribution

## Slide 61
Show some known facts about exponential distributions

## Slide 62: (on average)

## Slide 63: Question
You are waiting in front of your professor’s office. There is a note on the door
      Back in Exp(1/15) minutes
Questions
What is the probability that you wait
  less than 5 minutes?
  more than 10 minutes?
  exactly 10 minutes?
  between 10 and 25 minutes?
What is the expected amount you have to wait?
You have been waiting for 15 minutes
  What is the probability that you still have to wait less than 5 minutes?
  What is the probability that you still have to wait more than 10 minutes?
  exactly 10 minutes?
  between 10 and 25 minutes?
Reminder: P[X ≤ x] = 1 − e−λx

## Slide 64: Question
You are waiting in front of your professor’s office. There is a note on the door
      Back in Exp(1/15) minutes.
      X denotes your waiting time. Then X~ Exp(1/15)
Questions
What is the probability that you wait
  less than 5 minutes? P[X < 5] = 1 − e−5/15
  more than 10 minutes? P[X > 10] = e−10/15
  exactly 10 minutes? P[X = 10] = 0
  between 10 and 25 minutes? P[10 < X < 25] = P[X < 25] – P[ X < 10] =
  1 − e−25/15 - (1− e−10/15) = − e−25/15 + e−10/15
What is the expected amount you have to wait? E[X] = 15

## Slide 65: Question
You are waiting in front of your professor’s office. There is a note on the door
      Back in Exp(1/15) minutes.
      X denotes your waiting time. Then X~ Exp(1/15)
Questions
You have been waiting for 15 minutes
  What is the probability that you have to wait more than 10 minutes?
  P[ X > 25 | X > 15 ] =
  P[ X > 25 & X > 15 ] / P[ X > 15 ] =
  P[ X > 25 ] / P[ X > 15 ] =
  e−25/15 / e−15/15 = {use eaeb = ea+b}
  e−25/15 +15/15 =
  e−10/15 =
  P[ X > 10]
  Exponential distribution memoryless: past waiting time has not influence on future waiting time
  Note: can be approximated with a dice

## Slide 66: Question
You are waiting in front of your professor’s office. There is a note on the door
      Back in Exp(1/15) minutes.
      X denotes your waiting time. Then X~ Exp(1/15)
Questions
3. You have been waiting for 15 minutes
  What is the probability that you have to wait less than 5 minutes? 1 − e−5/15
  What is the probability that you have to wait more than 10 minutes? e−10/15
  exactly 10 minutes? P[X > 10] = 0
  between 10 and 25 minutes? − e−25/15 + e−10/15

## Slide 67: Example: probabilistic analysis
λ2
road trip
car
λ4
tire 1
λ4
tire 2
λ4
tire 3
λ4
tire 4
λ4
spare
2/5
phone
power
λ3
engine
battery
tires
λ1
connection
??
(p1 + p2 - p1p2)p3 +
p1(1 – ((1-p4)5 + 5p4(1-p4)4)(1-p3)
((1-e−λ1x) +
+ (1-e−λ2x) - (1-e−λ1x) (1-e−λ2x)) (1-e−λ3x)
+
(1-e−λ1x)(1 – (e−λ4x)5 + 5(e−λ4x) e−λ4x4)e−λ3x
Hint: If you’re smart, this can be fast

## Slide 68: Dynamic fault trees

## Slide 69: Dynamic fault trees: Safe road trip
car
tire 1
tire 2
tire 3
tire 4
spare
phone
connection
power
engine
battery
tires
road trip
Spares have reduced failure rates

## Slide 70: DFTs gates
static:
AND
OR
(k,m)
VOTING
dynamic: failure order matters
FDEP
SPARE
PAND
Previous restrictions
spare inputs: BEs
dep. events: BEs

## Slide 71: Dynamic fault trees: Qualitative analysis
car
tire 1
tire 2
tire 3
tire 4
spare
phone
connection
power
engine
battery
tires
road trip
Cut sets:
{Connection, engine}?
Yes, but order now matters

## Slide 72: Dynamic fault trees: Qualitative analysis
car
tire 1
tire 2
tire 3
tire 4
spare
phone
connection
power
engine
battery
tires
road trip
Cut sequences:
(Connection, engine)?
Need to consider negatives: (tire 1, tire 2, connection, engine)

## Slide 73: Fault tolerant parallel processors (FTPP)
NE1
NE3
N
E
2
N
E
4
Set up
4 types of processors available A, B, C, S
  Group S is a spare group
Connected via Network Elements
  If NE unavailable, all processors attached are unavailable
Requirement
for each type, at least 3 processors available
Question
Construct a (D)FT for this
A
B
C
S
A
B
C
S
A
B
C
S
A
B
C
S

## Slide 74: Fault tolerant parallel processors (FTPP)
System Failure
Group 1P Failure
2/4
A2
A3
A4
A1
Group 3P Failure
2/4
C2
C3
C4
C1
Group 2P Failure
2/4
B2
B3
B4
B1
Group 4 Failure
2/4
S2
S3
S4
S1
NE1
NE3
N
E
2
N
E
4
A
B
C
S
A
B
C
S
A
B
C
S
A
B
C
S
OR
FDEP
NE1
FDEP
NE2
FDEP
NE3
FDEP
NE4
A2
A3
A4
A1
C2
C3
C4
C1
B2
B3
B4
B1
S2
S3
S4
S1
Group A Failure
Group B Failure
Group C Failure
Requirement
for each type A, B, C
at least 3 processors available

## Slide 75: Fault tolerant parallel processors (FTPP)
System Failure
2/4
A2
A3
A4
A1
2/4
C2
C3
C4
C1
2/4
D2
D3
D4
D1
NE1
NE3
N
E
2
N
E
4
A
B
C
D
A
B
C
D
A
B
C
D
A
B
C
D
OR
FDEP
NE1
FDEP
NE2
FDEP
NE3
FDEP
NE4
A2
A3
A4
A1
C2
C3
C4
C1
B2
B3
B4
B1
D2
D3
D4
D1
Group B Failure
Group C Failure
Requirement
for each type A, B, C
at least 3 processors available
B2
B3
B4
B1
Group A Failure

## Slide 76: Fault tolerant parallel processors (FTPP)
System Failure
Group 1 Failure
2/4
OR
OR
OR
A2
A3
A4
A1
OR
Group 3 Failure
2/4
OR
OR
OR
C2
C3
C4
C1
OR
Group 2 Failure
2/4
OR
OR
OR
B2
B3
B4
B1
OR
Group 4 Failure
2/4
OR
OR
OR
D2
D3
D4
D1
OR
NE1
NE3
N
E
2
N
E
4
A
B
C
D
A
B
C
D
A
B
C
D
A
B
C
D
OR
NE1
NE3
NE4
NE2

## Slide 77: Dynamic fault trees: pitfalls
Simultaneous failures and PANDs:
Semi-spare nodes

## Slide 78: Dynamic fault trees: Quantitative analysis
Original method: Markov chains

## Slide 79: Dynamic fault trees: Analysis
car
tire 1
spare
phone
connection
power
engine
battery
road trip
tires
Draw the Markov chain for this simplified DFT.

## Slide 80: Dynamic fault trees: Solution
car
tire 1
spare
phone
connection
power
engine
battery
road trip
tires

## Slide 81: Fault tree analysis: how to compute reliability?
Failure
S
C
B
A
fail
1. Compositional
I/O-IMC Translation
Composition
2. Smart
Composition
CTMC
Difficult to validate,
modify
Goal:
Compute reliability, availability
Notes: Pijlen met vertaling en compositie

## Slide 82: Deep compositionality [IEEE TDSC’10]
Translation
Composition
+ hiding
minimization
Repeat
CTMC / CTMDP
Result:
unreliability
Analysis
MC generation
Order matters
(size only!)
1325 states
instead of
32757 states
= P[failure
during mission time]
Notes: Animation!

## Slide 83: Interactive Markov Chains (I/O-IMC)
I/O-Automata + CTMC
Markovian transitions (CTMC)
  labeled with rates λ
  delays governed by exponential distribution
  P[transition within t sec] = 1 – e- t
Interactive transitions (I/O)
  labeled with actions
  synchronization
Action signature
  ? - Input actions: delayable
  ! - Output actions: immediate
  ; - Internal actions: immediate
Recent work: discrete probabilty + costs
λ
fail!
I/O-IMC for
cold
basic event
act?
μ
fail!
Warm BE: can
fail before
activation,
with reduced rate

## Slide 84: Question: I/O-IMC semantics for DFT gates
fail(C)!
fail(A)?
fail(B)?
fail(B)?
fail(A)?
fail(C)!
fail(A)?
fail(B)?
fail(B)?
AND gate
PAND gate
Similar, but more complex for other gates

## Slide 85: Tool implementation: DFTcalc
DFTCalc
Metrics
Translation
Analysis
Efficiency:
Compositional aggregation
Context-dependent state space generation

## Slide 86: Challenge: state space explosion
Results:
reliability
availability
costs
strategy
diagnostics, …
stochastic
(Markov)
models
Reductions:
lumping
confluence
abstraction
….
Graph transformations
flatten ANDs, OR…

## Slide 88: Case studies & maintenance

## Slide 89: Integrating maintenance
Two new elements:
  Rate-dependency gate:
  Basic events with degradation and repairs:

## Slide 90: Case 1: Electrically Insulated Joint
Electrically separates tracks
45.000 EIJs in the Netherlands
Important cause of train disruptions

## Slide 91: Case 1: Electrically Insulated Joint

## Slide 92: Case 1: Electrically Insulated Joint (results)

## Slide 93: Case 2: Pneumatic compressor
Powers brakes, doors, etc.
Fail-safe but failures cause disruptions
Maintenance is essential for normal operation

## Slide 94: Case 2: Pneumatic compressor

## Slide 95: Case 2: Pneumatic compressor (results)

## Slide 96: Case 3: Oosterscheldekering
existing FT
  FT contains 1000’s of gates
  Leaves: spare part handeling
current strategy meets requirements